SMD5050 RGB LED Neonflex Strips

| Edit | Audit | Approve | Marketing |
| --- | --- | --- | --- |

- Product Feature

◇RGB LED Pixel neon strip for outdoor application

◇High lumen 5050 RGB LED

◇Double layer FPC

◇No dot with silicone tube

◇DC24V

◇6-LED cuttable

- Parameter

| Part No. | LED | LED Qty | Voltage | Current | Power | Dimension | IP Rank |
| --- | --- | --- | --- | --- | --- | --- | --- |
| TH-25050NEONRGB11-24 | 5050 | 300 | 24V | 3A | 72W | 5003*10*23mm | IP66 |

- Notice

- The product can only be used after the demolition of package. Before use, pls confirm the product have not been damaged in the transportation, if there has a demage it will not be able to install and use.

- Please choose the right LED power supply to operate when use, also please check the voltage range as well.

- The product best working environment temperature is -25℃ to 60℃, and storage temperature is -40℃ to 80℃.

- The product better installed in the ventilation place, it is not recommended to install in a sealed place, otherwise it will influence the heat dissipation of the products.

- Please cut off power supply when install, and then for electricity, please do not touch the product when using.

- Please attention electrostatic protection when use.

- According to the product of waterproof effect you can use indoor or outdoor use.

- To avoid eyes look straight into the light when use.

- Please follow the product instruction strictly.